## Slide 1: Open-sourece DTALite/NeXTA library based on GMNS
Dr. Xuesong (Simon) Zhou
xzhou74@asu.edu
Arizona State University
02/17, 2020

## Slide 2: 1.Quick introduction of DTAlite
Macroscopic assignment: --DTAlite (Static/Semi-dynamic assignment)
Mesoscopic assignment: --DTAlite (Dynamic assignment)

## Slide 3: Quick introduction of DTAlite
Macroscopic assignment: --DTAlite (Semi-dynamic assignment)
Mesoscopic assignment: --DTAlite (Dynamic assignment)
Microscopic assignment: --CAlite (Cellular Automatonassignment )

## Slide 4: Quick introduction of light-weight simulation tools
Welcome to STAlite (Light-weight computational engine of Static Traffic Assignment and Semi-dynamic assignment)
STAlite is an open-source AMS library for efficiently macroscopic traffic assignment
based on General Modeling Network Specification (GMNS) format
Network representation based on GMNS format
Extendable Volume Delay Function (VDF) functions：
  Standard BPR function
  BPR_X function that can obtain dynamic travel time efficiently
Path flow based internal representation to reach users equilibrium (UE)
Space time network based discrete event vehiclular simulation per 1 second
Enable dynamic OD demand estimation (ODME) using different data sources
Efficient multi-threading parallel computation and memory management, implemented in C++
Utilize up to 40 CPU cores, 200 GB of Memory for networks with more than 500K nodes

## Slide 5: 2. Network representation based on the General Modeling Network Specification (GMNS)

## Slide 6: Network representation based on GMNS github.com/zephyr-data-specs/GMNS
The objective of the General Modeling Network Specification (GMNS) is to provide a common human and machine-readable format for sharing routable road network files
  It is designed to be used in multi-resolution and multi-modal static and dynamic transportation planning and operations models
  It will facilitate the sharing of tools and data sources by modelers
The project is overseen by a project management group, with MPO, city, industry, academic and US DOT participation. In 2019, with support from the Federal Highway Administration, the team developed requirements and an initial release of the specification

## Slide 7: Network representation based on GMNS github.com/zephyr-data-specs/GMNS

## Slide 8: Network representation based on GMNS github.com/zephyr-data-specs/GMNS

## Slide 9: 3. Open-source Nexta AMS data hub for GMNS format

## Slide 10: Open-source Nexta AMS data hub for GMNS format

## Slide 11: Method 1 for creating network: Open-Source Network Downloader
https://pypi.org/project/osm2gmns/

## Slide 12: Method 2 for creating network: Multi-Level Network Convertor (Net2Cell)
https://pypi.org/project/net2cell/
Open-source tool for creating cell-based (microscopic) and mesoscopic and macro Networks
Produced by ASU NSF project: Real-time Management of Large Fleets of Self-Driving Vehicles Using Virtual Cyber Tracks
Macroscopic Network
Mesoscopic Network
Microscopic Network

## Slide 13: Method 3 for creating network: Convert GIS Shape File to GMNS CVS files
Shape files -> GMNS CVS files
Cube GIS files
TransCAD GIS files
VISUM GIS files

## Slide 14: Database development for using sensor data
Database development: Prepare the network configuration and link performance files in the database.
Data preparation mainly including network configuration and link performance file preparation.
Filegroup | Output file list | Remarks
Network | 1. node.csv 2. link.csv | Network representation based GMNS format
Observations | 3. link_performance.csv | (One-way) link-based speed and count data based on link format, for different resolutions

## Slide 15: High-Resolution Map
Phoenix Network | Data
# of nodes | 19,523
# of links | 47,712
# of zones | 3,022
# of agents for 24 hours | 10 million
Maryland Network | Data
# of nodes | 21,748
# of links | 62,232
# of zones | 1,598
# of agents for 24 hours | 18 million

## Slide 16: High-Resolution Map
Atlanta Network | Data
# of nodes | 26,988
# of links | 71,493
# of zones | 5,981
# of agents for 24 hours | 11.6 million
Philadelphia Network | Data
# of nodes | 86,853
# of links | 256,350
# of zones | 3,399
# of agents for 24 hours | 5.1 million

## Slide 17: Issues in Using Open Street Map in DTA model
The US Geological Survey has aerial imagery for the entire state of Maryland at a 6" resolution.
Fall 2007 to spring 2008: highest-resolution and newest imagery available for use in OpenStreetMap
Issues
  Traffic Analysis Zone Mapping
  Capacity values and number of lanes
  Signal data layers
  Connection with sensor data

## Slide 18: THANKS